## Slide 1
Chapter 2
Network Models

## Slide 2
2-1 LAYERED TASKS
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Sender, Receiver, and Carrier Hierarchy
Topics discussed in this section:

## Slide 3
Figure 2.1 Tasks involved in sending a letter

## Slide 4
4
Task of communication broken up into layers
Communication
Task
Layer 1
Layer 2
Layer 3
Layering

## Slide 5: Layers involving calling a friend
5

## Slide 6: Benefits of using a layered model
6
To find out the fault easily.
Changes in one layer do not affect other layers.
Have defined information that they act upon.

## Slide 7: Rules that govern communications
7
A protocol is a set of predetermined rules.
Defines:
  What is communicated??
  How it is communicated??
  When it is communicated??

## Slide 8: Protocols
8
Describe processes such as:
The format or structure of the message.
How and when error and system messages are passed between devices.
The setup and termination of data transfer sessions.
The method by which networking devices share information about pathways with other networks.
What?
How?
How/When?
What/When/How?

## Slide 9
9
Protocols and Standards
Protocols
Standards
Standards Organizations
Internet Standards

## Slide 10
10
Endorsed by the networking industry and approved by a standards organization.
Benefits:
  Create and maintain an open and competitive market.
  Ensured greater compatibility and interoperability.
Categories
De facto: Standards that have not been approved by an organized body but have been adopted as standards through widespread use
De jure: Those standards that have been legislated by an officially recognized body
Standards

## Slide 11: Standards and Protocols
11

## Slide 12
12
International Organization for Standardization (ISO)
Institute of Electrical and Electronic Engineers (IEEE)
American National Standards Institute (ANSI)
Telecommunications Industry Association (TIA)
The Internet Engineering Task Force (IETF)
International Telecommunications Union – Telecommunication Standards Sector (ITU-T)
Standard Organizations

## Slide 13
13
Layered standards:
OSI Reference model
  De Jure Standard
TCP/IP Protocol Model
  Open De Facto Standard
  Governed by IETF Working Groups
Communication Process

## Slide 14
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Layered Architecture Peer-to-Peer Processes
Encapsulation
Topics discussed in this section:

## Slide 15
ISO is the organization. OSI is the model.
Note

## Slide 16
Figure 2.2 Seven layers of the OSI model

## Slide 17: OSI Model- 7 Layers
17
Layers |  | 
7 | Application | 
6 | Presentation | 
5 | Session | 
4 | Transport | 
3 | Network | 
2 | Data Link | 
1 | Physical | 
Primary concern: Communications between applications
Primary concern: Moving raw data cross the network

## Slide 18
Figure 2.3 The interaction between layers in the OSI model

## Slide 19
19
An exchange using the OSI model

## Slide 20
2-3 LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed in this section:

## Slide 21: PHYSICAL LAYER
2.#
21

## Slide 22
22
Physical layer
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.

## Slide 23
23
Physical Characteristics of interfaces and medium.
Representation of bits
Data Rate
Synchronization of bits
Functions-Physical Layer

## Slide 24: Functions-Physical Layer
24
Physical Topology
  Bus
  Ring etc
Transmission Modes
  Simplex
  Half Duplex
  Full Duplex

## Slide 25: DATALINK LAYER
2.#
25

## Slide 26
26
Data link layer
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 27
27
Framing.
Physical Addressing
Flow Control
Error Control
Access Control
Functions-Data Link Layer
Data Link Layer PDU is called Frames.
Data Link Layer Protocol varies.

## Slide 28
28
Functions : Framing
Data
Header
H2
Data Link Layer
From Network Layer
Trailer
T2
To Physical Layer

## Slide 29
29
Hop-to-hop delivery

## Slide 30
30
Physical Address : MAC Address
07:01:02:01:2C:4B
Also known as MAC (Media Access Control) Address.
Every interface/port has an unique identifying number.
Given by manufacturer.
48 bits long, represented by 12 hexadecimal digits.

## Slide 31: Addressing
31
Sender
Receiver
A/11
IP address
MAC address
B/12
D/13
E/21
F/22
G/31
H/32
M/42
Assume:
IP Addresses – Alphabets
MAC Addresses - Numbers
A
M
11
13
D S D S
IP address
MAC address
A
M
21
22
M
31
32
A
A
M
41
N/41
42

## Slide 32
32
Addressing

## Slide 33: Addressing-Within the same network
33
A/11
B/12
D/14
C/13
Sender
Receiver
A
11
14
D
E/15
Assume:
IP Addresses – Alphabets
MAC Addresses - Numbers

## Slide 34: NETWORK LAYER
2.#
34

## Slide 35
35
Network layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 36: Example
36
LAN 1
LAN 2
LAN 3
Interconnections
Sender
Receiver
?
?
?
?

## Slide 37
37
Source-to-destination delivery
Functions :
  Adds an address to identify sender and receiver hosts.
  Decides which path to take.
A
F
Adds Logical Addressing
Routing

## Slide 38
38
Source-to-destination delivery
Network Layer PDU is called Packets.
Common Network layer Protocol is called Internet Protocol (IP)

## Slide 39
39
Universal address, each host uniquely defined.
32-bit address also known as IP Address.
Independent of underlying physical networks.
Logical Addresses :: IP Address
192.168.10.1 32 bits written in dotted decimal notation. Each decimal represented by 8 bits.

## Slide 40: TRANSPORT LAYER
2.#
40

## Slide 41
41
The transport layer is responsible for the delivery of a message from one process to another.
Transport layer

## Slide 42
42
Segmentation and Reassembly
Adds Port Address and Sequence Number.
Connection Control
Flow and Error Control
Multiplexing
Functions– Transport Layer
Transport Layer PDU is called Segments.
Common Protocol used in Transport Layer is TCP

## Slide 43
43
Transport layer
Segments data received from application layer into small parts.
Transport Layer Protocol Data Unit is called Segments.

## Slide 44: Function: Segmentation
44
Data from Application layer
Segments into small parts
Received by Transport Layer
1
Add a number to identify the application.
A1
A2
A1
A1
A1
Add a number sequence the segmented parts.
2
3
1
2
3

## Slide 45: Identifying Different Applications
45
Port Numbers

## Slide 46
46
To define multiple processes running in a computer.
16-bit in length
80
A 16-bit port address represented as one single number.
Port Address

## Slide 47: Function: Connection Control
47
Are you up?
Yes
Data

## Slide 48: Function: Flow Control
48
Data
Host A
Host B
Host B has too many packets to process.
Buffer to store incoming packets overflows
Please send less packets.

## Slide 49: Function: Error Control
49
Data
Host A
Host B
Please send packet 2.
Lost in transition
X
1
3
I have 1&3, where is 2?

## Slide 50
50
Functions– Multiplexing

## Slide 51: SESSION LAYER
2.#
51

## Slide 52
52
Session layer
The session layer is responsible for dialog control and synchronization.

## Slide 53
53
It handles the exchange of information
  to initiate dialogs,
  keep them active, and
  to restart sessions that are disrupted or idle for a long period of time
Most applications, like web browsers or e-mail clients, incorporate functionality of the OSI layers 5, 6 and 7.
53
Session Layer

## Slide 54: PRESENTATION LAYER
2.#
54

## Slide 55
55
Presentation layer
The presentation layer is responsible for translation, compression, and encryption.

## Slide 56
56
3 primary functions:
  Coding and conversion
  Compression of the data
  Encryption of the data
Presentation layer implementations are not typically associated with a particular protocol stack.
Presentation Layer

## Slide 57: APPLICATION LAYER
2.#
57

## Slide 58: Applications
58
The Interface Between Human and Data Networks
Responsible for providing services to the user.

## Slide 59
59
Applications in Application layer
Web Page
Email
Instant messaging

## Slide 60: Application Layer
60

## Slide 61
61
Applications in Application layer
Data
Header
H7
To Presentation Layer
Web Page
Email
Instant messaging

## Slide 62
62
Application layer
Data
Header
H7
From Presentation Layer
Web Page
Email
Instant messaging

## Slide 63
63
63
Application Layer
DNS
HTTP
SMTP
POP
DHCP
Examples of Protocols

## Slide 64
64
Summary of OSI Layers

## Slide 65
65
PDUs
Encapsulation
Headers and trailers
Summary

## Slide 66
66
TCP/IP
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network (ARPANET)
Used by the global Internet.
De Facto Standard

## Slide 67: TCP/IP Encapsulation
67

## Slide 68
68
TCP/IP and OSI model

## Slide 69
69
Addressing Summary
Four levels of addresses are used in an internet employing the TCP/IP protocols

## Slide 70
70
Relationship of layers and addresses in TCP/IP
IP Address
MAC Address

## Slide 71
71
Applications having user friendly addresses.
Email addresses or URLs.
  john@gmail.comjohn@gmail.com or www.bracu.ac.bd
These are converted into corresponding port and logical addresses by the sending computer.
Specific Addresses

## Slide 72: Addressing Review
72
Sender
Receiver
A/11
IP address
MAC address
B/12
D/13
E/21
F/22
G/31
H/32
M/42
Assume:
IP Addresses – Capital Alphabets
MAC Addresses – Numbers
Port Numbers- Small Alphabets
N/41
Email
a
Web
c
Email
k
k
a
A
M
11
13
D S D S D S

## Slide 73
73
Addressing Review
Although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.

## Slide 74: END
2.#
74